## Slide 1
FUNDAMENTALS OF ARTIFICIAL INTELLIGENCE
RULE\nENGINE
RTL → VCD → FACTS
Evidence-led diagnosis\nwith explainable rules
PROJECT PRESENTATION
Knowledge-Based Expert\nSystem for Digital Hardware\nDesign Debugging
Deterministic RTL and waveform-based debugging assistant
CHENTHAN AMUTHAN D • 2116240701090\nAMAR GANESH S • 2116240701035\nARSHAD AA • 2116240701050
October 2026

## Slide 2
01 / OVERVIEW
Abstract
A rule-driven assistant that connects design structure with observed signal behaviour.
02
Digital hardware debugging requires engineers to inspect RTL, testbench stimulus, simulation logs and waveforms together. This project combines these sources into one explainable workflow.\n\nPyVerilog extracts RTL facts; Icarus Verilog runs the simulation and creates a VCD; vcdvcd converts the VCD into machine-readable facts; and GTKWave displays the actual waveform. A Python inference engine applies explicit debugging rules and produces diagnoses with evidence and recommended fixes.\n\nIn the 4-bit counter case study, the system identified an enable signal held at 0 and a count register beginning at X.
INPUT
Verilog RTL + testbench
REASONING
Deterministic if–then rules
OUTPUT
Diagnosis + evidence + fix

## Slide 3
02 / NEED
Problem Statement
Debugging evidence is distributed, while interpretation is largely manual.
03
Distributed evidence
RTL, testbench stimulus, simulation output and waveforms must be inspected together.
Manual correlation
Cross-referencing signal behaviour by hand is time-consuming and can be error-prone.
Skill gap
Beginners may struggle with waveforms; experienced engineers repeat familiar checks.
Core problem: existing tools show what happened, but do not automatically correlate RTL structure and waveform behaviour to explain why.
Need: a structured, deterministic and explainable debugging assistant.

## Slide 4
03 / BACKGROUND
Literature Survey
The project builds on expert-system reasoning and established Verilog tools.
04
Rule-based expert systems
MYCIN demonstrated expert knowledge encoded as if–then rules with explanations. Standard systems combine a knowledge base, facts and an inference engine.
RTL parsing
PyVerilog provides a parser and exposes Verilog designs as an abstract syntax tree, enabling structural fact extraction.
Simulation and waveforms
Icarus Verilog simulates designs and can produce VCD files; GTKWave visualizes signal transitions over time.
Programmatic VCD analysis
vcdvcd reads signal names, transition times and values, making waveform behaviour available to software.
Key takeaway: these tools provide the building blocks; the project connects them with rule-based reasoning.

## Slide 5
04 / RESEARCH GAP
Research Gap
The gap identified in the project report is the missing link between evidence and explanation.
05
EXISTING TOOL ROLES
RTL inspection
Shows design structure
Simulator / waveform viewer
Shows signal behaviour
Engineer
Manually correlates both
IDENTIFIED GAP
No integrated, rule-driven pipeline automatically joins RTL facts with waveform facts and presents a traceable diagnosis with supporting evidence and a recommended fix.
Project response: combine parsing, simulation, waveform analysis and inference in one workflow.

## Slide 6
05 / AIM
Research Objectives
Six connected objectives guide the proposed system.
06
01
Parse RTL
Extract structural and behavioural facts from Verilog.
02
Automate simulation
Compile RTL + testbench and capture VCD output.
03
Analyze waveforms
Convert VCD transitions into machine-readable facts.
04
Apply rules
Fire explicit debugging rules against extracted facts.
05
Correlate evidence
Join RTL structure with waveform behaviour.
06
Generate diagnoses
Produce reports with evidence chains and recommendations.

## Slide 7
06 / PROPOSED WORK
System Architecture
Six-stage pipeline: from source files to an explainable debugging report.
07
INPUT
RTL + testbench
SIMULATION
Icarus Verilog → VCD
ANALYSIS
PyVerilog + vcdvcd
VISUALIZATION
GTKWave waveform
REASONING
Knowledge base + inference
OUTPUT
Explainable report
The same VCD is read by GTKWave for visual inspection and by vcdvcd for programmatic analysis.

## Slide 8
07 / METHOD
Algorithm (Software Model)
Deterministic processing sequence used to derive diagnoses.
08
1
Load RTL and testbench
2
Parse RTL with PyVerilog
3
Compile and simulate using iverilog + vvp
4
Generate vcdfile.vcd
5
Read VCD with vcdvcd; extract signal facts
6
Place RTL + waveform facts in working memory
7
Evaluate if–then rules and fire matching rules
8
Correlate evidence and generate report
Same inputs → same rules → same diagnosis (no learned or statistical model).

## Slide 9
08 / IMPLEMENTATION
Implementation (Software Model)
The implementation separates evidence collection, reasoning and presentation.
09
RTL parsing
PyVerilog AST traversal\nExtract module, ports, always block, reset and enable facts
Simulation
Compile RTL + testbench\nRun simulator and generate VCD
Waveform analysis
Read transitions, timestamps and values\nRecord initial value and constant signals
Inference + report
Match facts to named rules\nShow evidence chain and recommended fix
Frontend: displays GTKWave-rendered waveform beside inference results; “Open in GTKWave” enables native inspection.

## Slide 10
09 / EVALUATION
Output and Results
Case study: 4-bit synchronous counter with clk, rst and en inputs.
10
Signal
Transitions
Observed result
clk
13
Regular clock; expected behaviour
rst
5
Reset asserted and deasserted normally
en
1
Constant 0; potential testbench stimulus gap
count[3:0]
6
Initial value = X; possible uninitialized register
RULE 1 — ENABLE STUCK LOW
en = 0 throughout → counter increment blocked.
RULE 2 — UNINITIALIZED REGISTER
count begins at X → reset branch lacks a defined value.
Recommended fixes: assert en = 1 in the testbench; add count <= 0 in the RTL reset branch.

## Slide 11
10 / WRAP-UP
Conclusion and Future Work
The case study demonstrates evidence-based, explainable debugging.
11
Conclusion
The pipeline connected RTL parsing, simulation, VCD analysis and rule-based inference. It identified one stimulus-side issue and one RTL-side issue, with traceable evidence and fixes.
Current scope
Verilog designs simulatable with Icarus Verilog. The system is deterministic and supports engineer judgement rather than replacing it.
FUTURE WORK
• Add rules for clock/reset faults and unknown outputs
• Support larger multi-module designs and hierarchical signals
• Extend source support to SystemVerilog and VHDL
• Generate suggested testbench patches and RTL fixes
• Evaluate on more benchmark designs with known faults
Thank you